- A parallel-plate capacitor consists of two parallel conducting plates of area S separated by a uniform distance d. The space between the plates is filled with a dielectric of a constant permittivity . (15%)

(1) Determine the capacitance.

(2) As shown in Fig. 1, this capacitor is charged to a voltage V. Find the stored electrostatic energy.

Fig. 1

- Fig. 2 shows a simplified rotor and stator for a dc brushless motor. List and describe the types of losses that occur in the magnetic circuit of Fig. 2 for real-life conditions. (15%)

Fig. 2

- Explain the following terms (20%)

(1) Faraday’s Law

(2) Ampere’s law

(3) Proximity effect

(4) Hall effect

- Given  in the spherical coordinate system, determine the magnitude and direction of the maximum rate of increase of V at point (1, 1, 0).(15 %)

- Please show the characteristics of the electric fields for the cases of right-hand and left-hand circularly polarized waves. (15 %)

- A signal generator is to feed equal power through a lossless air transmission line with a characteristic impedance 50 (Ω) to two separate resistive loads, 64 (Ω) and 25 (Ω). Quarter-wave transformers are used to match the loads to the 50 (Ω) lines. (20 %)

(1) Derive the required characteristic impedances of the quarter-wave lines.

(2) Find the standing-wave ratios on the matching line sections.

# Text boxes

電機工程學系碩士班

國立臺南大學105學年度 　    　　　　　　　　 招生考試  電磁學  試題卷